## Slide 1: ENG4118/5326 - Robotics 4/M Sensors, Actuators and Image capture, processing and analysis
Lecture 2
Kevin Worrall

## Slide 2: Overview
Sensor Performance Specifications
  What are sensor specifications?
  Parameters

## Slide 3: What is measurement?
We measure everything…
measurement is information about a physical quantity
And to make a measurement we need a sensor
A sensor facilitates the transfer of information about a physical quantity
But measurement is never prefect
  Errors are present in the sensing device
  The sensing device can change the measurement
Need to understand the sensor specifications

## Slide 4: Sensor Specifications
sensor specifications quantify the ability of a sensor to provide measurements of physical variables
This in turn allows you to interpret the output from the sensor and match it to the input (what you are wanting to know about)
To support this sensor manufacturers create datasheets

## Slide 5: Datasheet Examples
Temperature Sensor 1:
  https://www.ti.com/lit/ds/symlink/lmt86.pdf
Temperature Sensor 2 :
  https://www.ti.com/lit/ds/symlink/lm235.pdf
Accelerometer:
  https://www.analog.com/media/en/technical-documentation/data-sheets/adxl345.pdf

## Slide 6: Physical Principles Applied to Sensors

## Slide 7: Sensor Physics
What physical principles are used to allow sensors to react to, then provide an output regarding the environment?
Often what we want to measure must be converted into a different signal
And we often are not measuring the parameter directly but the influence of the parameter
Important to keep this in mind when selecting sensors
  What is the most appropriate way to measure the parameter in your system

## Slide 8: Sensor Physics
Resistive An electrical potential difference produces a current and vice versa (Ohm's Law: I = V/R)
  Many Temperature Sensors
Capacitive Capacitance changes due to movement of conducting plates or insulating material between plates
  Touch Screen, some accelerometers, touch pads
Inductive Changes in inductance due to movement of a magnetic core material or coil
  Metal Detectors
Piezoelectric Strain produces charge in specific materials e.g. Zirconium Titanante
  Strain gauges

## Slide 9: Sensor Physics
Hall Effect A magnetic field induces an electric potential
  Wheel Encoders
Optical Several principles used, including light intensity, interferometry, Doppler, holography, reflection and modulation
  Vision systems, light sensor
Optical Several principles used, including light intensity, interferometry, Doppler, holography, reflection and modulation
  Vision systems, light sensor

## Slide 10: Sensor Specifications

## Slide 11: Keep in mind
Measurements can be:
  Time-independent: length, mass
  Time-dependant: acceleration
  Relative: relative to another measurement
  Absolute: actual value

## Slide 12: Static and Dynamic Response
Static Response
  characterises the sensor output after all transients have dissipated
  Output of the sensor when a steady state condition occurs
Dynamic Response
  Sensor behaviour between the time of a change of input to the time the sensor settles
  Different sensors have different responses

## Slide 13: Static Response - Linear
Chart: Static Response
| 0 | 2 | 4 | 6 | 8 | 10 | 12 | 14
 | 0 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5

## Slide 14: Static Response - Offset
Chart: Static Response with Offset
| 0 | 2 | 4 | 6 | 8 | 10 | 12 | 14
 | 0.3 | 0.8 | 1.3 | 1.8 | 2.3 | 2.8 | 3.3 | 3.8

## Slide 15: Static Response – Non-Linear
Chart: Static Response - Non Linear
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
 | 0.5 | 0.52 | 0.55 | 0.6 | 0.72 | 1 | 2 | 2.7 | 2.9 | 3 | 3.1 | 3.2 | 3.25 | 3.27
Sometimes only the linear area is used

## Slide 16: Static Response
Chart: Static Responses
| 0 | 2 | 4 | 6 | 8 | 10 | 12 | 14
Normal | 0 | 0.5 | 1 | 1.5 | 2 | 2.5 | 3 | 3.5
with Offset | 0.3 | 0.8 | 1.3 | 1.8 | 2.3 | 2.8 | 3.3 | 3.8
Non Linear | 0.5 | 0.52 | 0.55 | 0.6 | 0.72 | 1 | 2 | 2.7 | 2.9 | 3 | 3.1 | 3.2 | 3.25 | 3.27

## Slide 17: Static Response – Non-Linear
Most static response curves are one to one
  A given input value will result in a given output value
  In theory
    But there are always exceptions

## Slide 18: Static Response

## Slide 19: Dynamic Response
Response Time
  time taken until the sensor output matches a percentage value of the sensor input.
Time Constant
  63.2% response time. How fast the sensor reacts to changes in the input.
Rise Time
  Time taken to reach a particular value
Settling Time
  Time taken to settle to within a percentage of the steady state value

## Slide 20: Range and Span
Range
  defines the limits between which the input can vary
Span
  is the maximum value minus the minimum value
Example
  Temperature Sensor Range -45°C to +150°C
  Span is 195°C
Your application dictates the required range
If your system will only ever operate in an environment that varies between 23°C and 27°C then get a sensor that works well in that range...

## Slide 21: Accuracy
The extent to which the value returned by the sensor might be wrong
Summation of all possible errors that are likely to occur, as well as the 'as supplied' calibration (which could be none)
Typically given as a ± value or percentage
Fundamental and normally most important aspect

## Slide 22: Accuracy
Temperature Sensor accuracy of ±2°C
  Means that value returned is within ±2°C of actual
  +25°C returned could mean anything from 23°C to 27°C
Consider the application
  Temperature Sensor, accuracy of ±5% over full range
  Range is 0 to +200°C, accuracy is (200*0.05) ±10°C
  So at +25°C sensor can return +15°C to +35°C

## Slide 23: Accuracy
Learn to be wary of how accuracy is stated
Manufacturers will state numbers in the best light
Which is best?
  0-150°C @ ±6°C
  0-150°C @ ±5% full scale
  69 < 75 < 81°C or 67.5 < 75 < 82.5°C
Be wary of percentages
  1% of 1000°C is 10°C, 1% of 100°C is 1°C...
If you are unsure – do the maths…

## Slide 24: Error
Error
  defined as the difference between the sensor output and the true value of the quantity being read
  Returned value is 23°C, true is 21°C error is (23-21) 2°C
Error is sometimes used to describe other aspects of the sensor... better to be specific... detail later!

## Slide 25: Sensitivity
How much the output changes by when the input changes
Relationship between the output and input:
But can also be used to describe effect on input from environmental changes
Pressure sensor may have a temperature sensitivity of ±0.1% per °C
Assuming fixed output span
  Static Response curves with high sensitivity have small input range
  Static Response curves with low sensitivity have large input range

## Slide 26: Sensitivity
Chart: Sensitivity Comparsion
| 0 | 2 | 4 | 6 | 8 | 10 | 12 | 14
Low Sensitivity | 0.3 | 0.8 | 1.3 | 1.8 | 2.3 | 2.8 | 3.3 | 3.8
High Sensitivity | 0.3 | 2.3 | 4.3 | 6.3 | 8.3 | 10.3 | 12.3 | 14.3
Fixed Width
Small input width
Large input width

## Slide 27: Hysteresis
Some sensors can give different readings for the same input depending on the whether the sensor input was increasing or decreasing
Reading is based on the current input as well as the history of inputs
Not necessarily a bad thing, depending on application
...but ideal would be not to have any

## Slide 28: Hysteresis
Chart: Hysteresis
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
 | 0.5 | 0.52 | 0.55 | 0.6 | 0.72 | 1 | 2 | 2.7 | 2.9 | 3 | 3.1 | 3.2 | 3.25 | 3.27
 | 0.5 | 0.52 | 0.55 | 0.58 | 0.6 | 0.72 | 1 | 2 | 2.7 | 2.9 | 3 | 3.1 | 3.2 | 3.27

## Slide 29: Non-Linearity Error
Normally a linear relationship is assumed between input and output
This is not usually the case, and the maximum difference between the ideal linear relationship and the actual value is the Non-Linearity Error
Typically quoted as a percentage
  Non-linearity Error is ±0.05%
Method used to calculate linear relationship
  Was the line drawn between the max' and min' values?
  Was it drawn through the zero point?
  Best fit for a range of points?
  Assumed operating point?

## Slide 30: Repeatability
Ability to give the same output for repeated applications of the same input
Another percentage:
Repeatability is limited by hysteresis and noise
If repeatability is good, then noise and hysteresis must be small

## Slide 31: Review
What are sensor specifications?
Parameters
  Static and Dynamic Response
  Range and Span
  Accuracy
  Error
  Sensitivity
  Hysteresis
  Non-Linearity Error
  Repeatability

## Slide 32: References
Please read:
  Bernstein, D. S. “A student’s guide to sensor performance specifications”, IEEE Control Systems Magazine, 21, 4, 9-18, 2001
  Bernstein, D. S. Sensor Performance Specifications, IEEE Control Systems Magazine, 21, 4, 9-18, 2001
Bolton, W., Mechatronics, 5th Edition, Pearson, 2012
  Chapter 2 - Sections 2.1 and 2.2