## Slide 1: ENG4118/5326 - Robotics 4/M Sensors, Actuators and Image capture, processing and analysis
Lecture 4
Kevin Worrall

## Slide 2: Sensor Connection

## Slide 3: Sensor Connection
Need to be aware that your sensor needs to connect to something
  Logging system
  Communication bus
  Microcontroller
  Analog to digital convertor
  …
Expectation is that this connection will be perfect
  What the sensor reads is what the system that is connected to it reads
…but…
You are introducing additional sources of everything we have discussed

## Slide 4: Sensor Connection
Most common example is a sensor that outputs a voltage…
More on this particular example later but there is an instant change…
Your output is no longer a relationship between Vs and Vout (as you will find in a data sheet) but actually Vs and VI
But…

## Slide 5: Sensor Connection
Voltage and current measurements need an interface
  Impedance
  Noise
Pins, wires, connectors, cable lengths… can all impact
Is your analogue interface suitable?
  does your Analogue to Digital converter have a good resolution?
But what about digital interfaces?
  Timing – is your sensor the only one on the bus?
    Can you detect and react within a suitable timeframe?
  What is the actual speed of the network and the actual time stamp?
  If you have a 24-bit output from a signal but a 16-bit processor – how do you ensure that you don’t lose information?

## Slide 6: Sensor Modelling

## Slide 7: Sensor Modelling
It can help to consider a single sensor as a system
  Input
  Disturbances
  Desired
  Output
Fundamentally a general sensor equation can be given as:
Where y is the output, f is a sensor function, x is the sensor input, a represents internal parameters, c is a constant

## Slide 8: Sensor Modelling
There are general models of sensors
Hammerstien-Wiener feedback model is one

## Slide 9: Sensor Modelling
Input
Output

## Slide 10: Sensor Modelling
Input
Output
Noise
Noise
Bias
Saturation
Saturation
Previous Measurements
Dead band
Hysteresis
And that’s before you factor in the connection

## Slide 11: Example

## Slide 12: Temperature Sensor – LMT86
Accurate - ±0.4°C but maximum ±2.7°C
Gain -10.9mv/°C
Range -50°C to 150°C
Thermal time constant 10s (1.2m/s airflow)
Various other but these are the important parameters for us
So what does this mean?

## Slide 13: Temperature Sensor – LMT86
Chart: LMT86

## Slide 14: Temperature Sensor – LMT86
Chart: LMT86

## Slide 15: Temperature Sensor – LMT86
Chart: 

## Slide 16: Temperature Sensor – LMT86
Chart: 

## Slide 17: Temperature Sensor – LMT86
Conversion of voltage
Output voltage – 2616mV to 420mV (-50°C to 150°C)
Need to detect about 1mV
8 bit AtoD – 256 discreet (assuming 3V reference) 11.7mV… this can be done… but only ever going to get 1°C as a result of the calibration data available in the datasheet.

## Slide 18: Examples
Further examples will be made available

## Slide 19: Overview
Position and displacement Sensors
  Overview
  Potentiometers
  LVDT
  Resolvers

## Slide 20: Position and Displacement Sensors

## Slide 21: Position and Displacement
Position Sensors Concerned with the determination of the position of some object in relation to some reference point
Displacement Sensors Concerned with the measurement of the amount by which some object has moved
Contact Sensors the object being sensed comes into mechanical contact with the sensor
Non-Contact Sensors there is no physical contact between the object being sensed and the sensor

## Slide 22: Position and Displacement - Examples
Position
  How far from the charging station?
  How close is the end effector to the input tray?
Position Sensor
  Ruler, protractor
  Encoders
  Linear and angular variable resistors
  Draw string sensors
Displacement
  How for has the mobile robot moved?
Displacement sensor
  Normally the same devices are used but you are measuring from a different point

## Slide 23: Potentiometers

## Slide 24: Potentiometers
What can potentiometers be used for?
  Provide the position (with suitable calculations) of rotational joints
  A potentiometer converts position information into a variable voltage through a resistor
As the sliding contact (wiper) slides along the resistor, the proportion of resistance before or after the wiper contact point varies compared to the total resistance
With a constant input voltage, VS, the output voltage, Vout, is a fraction of the input voltage

## Slide 25: Potentiometers
Potentiometers are available in both linear and rotary forms and can be used to measure linear or angular motion
The resistor is in the form of a track along the potentiometer
This track may be of thin film of a resistive material such as carbon, conductive ceramic, conductive plastic or metal
Alternatively wire wound potentiometers are used with the track consisting of a highly resistive wire wound on to anodised aluminium
https://www.build-electronic-circuits.com/potentiometer/

## Slide 26: Potentiometers
Input voltage, Vs, is between terminals 1 and 3
Output voltage is between terminals 2 and 3.
With a constant input voltage, VS, the output voltage, Vout, is a fraction of the input voltage

## Slide 27: Potentiometers
An important effect to be considered with potentiometers is the effect of load, Rl, connected across the output.

## Slide 28: Potentiometers
The potential difference across the load, Vl, is only directly proportional to the output voltage, Vout, if the load resistance, Rl, is infinite
For loads of finite resistance, the effect of the load is to transform the linear relationship between voltage and displacement into a non-linear relationship
To find the total resistance across the input voltage we analyse the circuit

## Slide 29: Potentiometers
Full Calculation is:
With x being a fraction of Rp
However…

## Slide 30: Potentiometers
Error introduced by load having finite resistance is:

## Slide 31: Potentiometers - Error
Example - 500Ω with slider 1/2 along the track, Rl 10kΩ, Vs 4V
  As a percentage of fullscale input range this 0.625% (0.025/4 * 100)
Example - 500Ω with slider 1/2 along the track, Rl 50kΩ, Vs 4V
  As a percentage of fullscale input range this 0.125% (0.005/4 * 100)
This shows the difference Rl can make.

## Slide 32: Potentiometers
Problems with wiper wear are significant and result from the friction between the wiper and track
Reliability improved by minimising current drawn from wiper contact
Provide absolute position information at relatively low cost (unless very high accuracy needed)

## Slide 33: Linear Variable Differential Transformer

## Slide 34: Linear Variable Differential Transformer
LVDT for short
Widely used as primary sensors for monitoring displacements
Consists of three coils symmetrically spaced along an insulated tube.
The central coil is the primary coil and the other two are identical secondary coils which are connected such that their outputs oppose each other.
Measurements made through the movement of a magnetic core which results from the displacement of the probe tip.
https://singer-instruments.com/introduction-to-lvdt/

## Slide 35: Linear Variable Differential Transformer
When an alternating voltage input is applied to the primary coil, alternating emf′s are induced in the secondary coils
With the magnetic core central, the amount of magnetic material within each of the secondary coils is equal and the emf′s produced in each coil are the same with the net result being zero output
When the core is displaced from the central position, due to probe displacement, there is a greater amount of the core in one of the secondary coils than the other
This results in a greater emf being induced in one coil than the other which produces a non-zero output
The sensor output, the difference between the two emf’s increases with increased displacement
Or… https://www.youtube.com/watch?v=08yKYiZv-kg

## Slide 36: Linear Variable Differential Transformer
The emf induced in a secondary coil by a changing current i in the primary coil is given by:
M is the mutual inductance which is dependent on the number of turns on the coils and the composition of the core
For a sinusoidal input current of i = isinωt to the primary coil, the emf’s induced in the two secondary coils are:

## Slide 37: Linear Variable Differential Transformer
The values of kA, kB and φ depend on the degree of coupling between the primary and secondary coils for a particular core position
φ is the phase difference between the primary alternating voltage and that of the secondary coils
The LVDT is the difference between the two secondary coils given by:
When the core is equally in both coils ka = kb and the output voltage is zero

## Slide 38: Linear Variable Differential Transformer
When the core is more in secondary coil a than in b we have ka > kb :
When the core is more in secondary coil b than in a we have ka < kb and there is a phase change of 180:
or
The output voltage and phase for varying displacements are shown for the secondary coils in the following slide

## Slide 39: Linear Variable Differential Transformer

## Slide 40: Linear Variable Differential Transformer
With this type of output the same output voltage amplitude is produced for two different displacements
To distinguish between displacements, we need to distinguish them using the phase of their output voltage
A phase sensitive demodulator, with a low pass filter, is used to convert the output into d.c. voltage which gives a unique value for each displacement

## Slide 41: Linear Variable Differential Transformer
LVDTs are rugged devices compared to potentiometers and can be used as secondary sensors for the measurement of Force, Weight or Pressure.
They have operating ranges between ±2 to ±400mm with non-linearity errors of around ±0.25%
They are also very accurate, with accuracies from 0.5% to 0.05% typically, but require external support circuitry
Resolution limited by presence of the null voltage (exact cancellation of secondary voltages not possible due to different phase shifts in the two windings).

## Slide 42: Resolver

## Slide 43: Resolvers
Resolvers are like LVDTs in principle but are used to measure angular motion
A resolver is also a transformer where the primary coil is attached to the rotating shaft and carries an alternating current, either through slip rings or from a brush-less transformer within it
There are two secondary coils positioned 90° apart from each other
As the rotor rotates the flux it develops rotates with it

## Slide 44: Resolvers
When the primary coil is parallel to either of the secondary coils the voltage induced in the coils is maximum

## Slide 45: Resolvers
At this instant the primary coil is perpendicular to the other secondary coil and no voltage is developed within it
As the primary coil rotates the voltage in the first secondary coil goes to zero whilst the voltage of the other secondary coil becomes maximum
For all angles in between the two secondary coils develop a voltage proportional to the sine and cosine of the angle between the primary and secondary coils
Resolvers are reliable, robust and accurate
  Accuracy more dependant on the sensing circuitary
However, resolvers are significantly more expensive than potentiometers
High speeds up to 20000RPM

## Slide 46: Review
Overview
Potentiometers
LVDT
Resolvers

## Slide 47: References
Bolton, W., Mechatronics, 5th Edition, Pearson, 2012
  Chapter 2 - Sections 2.1 and 2.2
Niku, S.B. , Introduction to Robotics, 2nd Edition, Wiley, New Jersey, 2011.