## Slide 1: ENG4118/5326 - Robotics 4/M Sensors, Actuators and Image capture, processing and analysis
Lecture 6
Kevin Worrall

## Slide 2: Overview
Optical Encoders
Velocity Sensors
Rate Gyroscope
Acceleration Sensors
Review

## Slide 3: Optical Encoders

## Slide 4: Optical Encoders
Encoder is a device which provides a digital output in relation to an angular displacement
Position encoders falls into two categories Incremental or Absolute
Incremental encoders detect changes in position from some reference (datum) position
Absolute encoders give actual angular position
The advantage of this type of sensor is that they are contactless detectors which avoid wear issues but must be kept clean

## Slide 5: Optical Encoders
Incremental encoders utilise a light source and light detector
The light source passes through slots in the disk and is detected by the light detector.
When the disk is rotated a pulsed output is produced by the detector with the number of pulses produced being proportional to the angle through which the disk has rotated

## Slide 6: Optical Encoders
In practice three concentric disk tracks are used with three LED/detector pairs.
The innermost ring has a single hole and is used to locate the home position of the disk
The two outer tracks have a series of equally spaced holes which are offset to one another which allows the direction of rotation to be determined
In a clockwise rotation, the pulses from the outer track lead those from the inner track and the opposite is true for the anti-clockwise direction
Encoder resolution is determined by the number of slots on the disk e.g. for 60 slots in 1 revolution the resolution is 360°/ 60=6°

## Slide 7: Optical Encoders
Absolute encoders produce a unique code for every position of shaft
The output from the detector is in the form of a binary number
The rotating disk opposite has four concentric circles of slots and four detectors to detect the light pulses

## Slide 8: Optical Encoders
These slots are arranged such that the sequential output from the detectors is a number in binary code
Typical encoders have up to 10 or 12 tracks and the number of bits in the binary number will be equal to the number of tracks
Thus with 10 tracks there will be 10 bits so the number of positions that can be detected is 2^10 =1024
This gives a resolution of 360°/ 1024=0.35° for a single rotation of the disk
The normal form of binary code isn’t used since changing from one binary number to the next can result in more than one bit changing
To overcome this Gray Code is used with only one bit changing from one number to the next.

## Slide 9: Optical Encoders
Decimal | Binary | Gray
0 | 0000 | 0000
1 | 0001 | 0001
2 | 0010 | 0011
3 | 0011 | 0010
4 | 0100 | 0110
5 | 0101 | 0111
6 | 0110 | 0101
7 | 0111 | 0100
8 | 1000 | 1100

## Slide 10: Optical Encoders
Incremental Encoder
  https://www.youtube.com/watch?v=zzHcsJDV3_o
Absolute Encoder
  https://www.youtube.com/watch?v=yOmYCh_i_JI

## Slide 11: Velocity Sensors

## Slide 12: Velocity Sensors
Designed to measure the velocity of the system
With some calculations incremental encoders can be used as velocity sensors
Other velocity sensors exist...
  Keep in mind Appropriate use!

## Slide 13: Velocity Sensors
Tachometer
  A tachometer is a generator which converts mechanical energy into electrical energy
  Its output is an analogue voltage proportional to the input angular speed.
  Tachometers are generally inaccurate at very low speeds
  Non-linearity for these sensors is typically ±0.15% and they can operate up to speeds of 10,000 rpm

## Slide 14: Velocity Sensors
Variable reluctance tachometer
  Uses a toothed wheel of ferromagnetic material which is connected to a rotating shaft and a coil to sense angular velocity again using a process of counting pulses.

## Slide 15: Velocity Sensors
A pickup coil is wound around a permanent magnet and as the wheel rotates the teeth move past the coil thus changing the air gap between the ferromagnetic material and the coil
The changing flux due to the change in air gap between the coil and ferromagnetic teeth produces an alternating emf in the coil
If the wheel has n teeth and rotates with angular velocity ω, the flux change with time is of the form:
Φ = Φ0+ ΦV cos(n.ω.t)
Where Φ0 is the mean value of the flux and ΦV is the amplitude of flux variation due to the presence of the toothed wheel

## Slide 16: Velocity Sensors
The induced emf in the N turns of the pickup coil is given by:
where the maximum value of the induced emf is
and is thus a measure of the angular velocity

## Slide 17: Rate Gyroscope

## Slide 18: Rate Gyroscope
Rate Gyroscopes
  Measures rate of change of angle with time
  Very common
  Accuracy varies, as does the price
  Very fast to respond
  Different ranges exist <±50°s-1 to >±1000°s-1

## Slide 19: Rate Gyroscope
Various technologies exist
  From laser to mems
  MEMs (MicroElectroMechanical systems )
    mechanical devices built onto semiconductor chips
    Consist of microprocessor, micro-sensors and micro-actuators and can sense, control and activate mechanical processes on a micro-scale.
    MEMS range in size from 20 micrometres to 1mm with components 0.001 to 0.1 mm in size
Introduction to MEMs Gyroscope
  https://www.youtube.com/watch?v=XsjvaYAFN1M
Basic principle is that an angular acceleration affects the system and this effect is detected
Principle use is to detect the angular speed of a system
Output can be integrated to get angular position

## Slide 20: Acceleration Sensors

## Slide 21: Acceleration Sensors
Accelerometers measure the accelerations along the axis that the accelerometers have been attached to
The design of an accelerometer is varied
  Some use a mass on beam that in turn is connected to a potentiometer
  Some are based on a capacitive effect
  Others are piezoelectric or piezoresistive
  And some can be LVDT based...

## Slide 22: Acceleration Sensors
LVDT Method
  The sensor detects acceleration by sensing the displacement of a mass restrained by a spring with a dashpot providing viscous resistance.
  The force exerted by the spring is proportional to spring extension (Hook’s Law) and force exerted by the dashpot is proportional to the LVDT shaft velocity.

## Slide 23: Acceleration Sensors
Most accelerometers you will come across are MEMs devices
MEMs based:
  https://www.youtube.com/watch?v=4kfzqZpttTA

## Slide 24: Acceleration Sensors
Applications
  Measuring Acceleration
  Detecting Accelerations
    Air bags are often the example used
  Output can be integrated for velocity
Issues
  Drift
  Often need reset with an external source
  Output is either filtered or requires to be filtered

## Slide 25: Review
Optical Encoders
Velocity Sensors
Rate Gyroscope
Acceleration Sensors

## Slide 26: References
Bolton, W., Mechatronics, 5th Edition, Pearson, 2012
  Chapter 2 - Sections 2.1 and 2.2
Niku, S.B. , Introduction to Robotics, 2nd Edition, Wiley, New Jersey, 2011.