## Slide 1: ENG4118/5326 - Robotics 4/M Sensors, Actuators and Image capture, processing and analysis
Lecture 9
Kevin Worrall

## Slide 2: Lecture Overview
More sensors

## Slide 3: Visual Sensors
Covered in another section of the course
  Image capture
  Image processing
  Image analysis
  And applications
    Vision
    Stereo Vision
    Motion tracking
A lot to take in

## Slide 4: Other Sensors
There are many other sensors that we have not yet discussed but are in wide use
  Sound and Voice
  Compasses
  IMU
  Motion tracking
  GPS
This lecture aims to introduce these concepts

## Slide 5: Sound and Voice

## Slide 6: Sound
Sound sensor detects a sound
Sensors converts into an electrical signal
Electrical signal is digitised and can be analysed to interpret the sound wave detected
Sound Sensor
  Microphone

## Slide 7: Sound
Different type of microphones
Condenser type is one
  Sound waves strike a diaphragm,
  This changes the distance to a second fixed plate
  Using the capacitive effect an output signal is created
  This output can be measured

## Slide 8: Sound
Interface circuits
  Many different types
  Some will just return that a sound within a set frequency was heard
  Others will pass on the complete range of signals heard – this would need further analysis
Different uses
  Detect noise within workspace
  Detect commands

## Slide 9: Voice Recognition
Involves determining what is said and taking an action based on the perceived information.
Works on the frequency content of spoken words.
Every word is decomposed into its constituent frequencies with a unique signature. Allows the system to recognize the word.
The user must train the system by speaking the words a priori.
  Speech recognition
  Machine learning algorithms

## Slide 10: Voice Recognition
Creates a look-up table of the major frequencies.
Tries to match with the information in the look-up table.
Recognition affected by variations in volume, accent, speed, etc.
More accurate look-up table makes recognition more difficult.
Requires processing power to do this accurately but simple systems can be easily created

## Slide 11: Compasses

## Slide 12: Compasses
Navigational device
Shows direction relative to the Earth’s magnetic field
Can provide a fixed point for reference for a mobile robot or an additional fixed reference point for a manipulator

## Slide 13: Compasses
For robotics – Magnetometers are usually used
  Normally in a triaxial configuration
Can detect the magnetic field about the sensor
  Like haff effect sensors but can provide details about the magnetic field
Normally used to detect the strength of a magnetic field
With some coding the number of degrees from North can be calculated – hence the compass
Accelerometers are normally included so the Earths “down” (gravity vector) can be detected
  Compensates for tilt etc

## Slide 14: Compasses
Main uses
  Providing a reference point
  heading control for mobile robots
  Can be used to measure the angle from a set magnetic field point
  External motion control
Be aware of the drawbacks
  Other Magnetic fields can alter the measurements
  Steel in buildings and surroundings can alter the magnetic field

## Slide 15: IMU

## Slide 16: IMU
Inertia Measurement Unit
Made up of
  Accelerometers
  Rate Gyroscopes
  Magnetometers
Various constructs
  MEMs based
    Allows for digital interfacing and filtering to be done on aboard

## Slide 17: IMU
The theory behind the main components has been covered
IMUs combine more than these though
  Temperature sensor
  Signal conditioning
  External interface
  Motion processes
Typically, onboard software
  Filtering
  Sensor fusion

## Slide 18: IMU
But why integrate all these?
  Motion of the system can be referenced to this single point
  The output of each sensor can compensate for the output of the other sensors
What can the IMU be used for?
  In place of the single sensors provided before – providing more information
  Motion sensing
    AR, VR
    Robotics in general

## Slide 19: Motion Tracking

## Slide 20: Motion tracking
Sometime internal sensors are not enough or do not provide a full picture of the current operational environment
Need to look at the system AND the environment
Motion tracking is used for this
  Films and video games use this as motion capture

## Slide 21: Motion tracking
Many different approaches
  Visual,
  Infrared,
  Magnetic
Markers are normally placed in critical areas of the system
These are tracked by using a series of cameras
Triangulation is then used
Some systems claim μm precision

## Slide 22: Motion tracking
Magnetic system operates in a similar way
  Base station emits emf
  Receivers pick this up and reflect the signal back
  Triangulation can be used but normally systems are more advanced

## Slide 23: Motion tracking
Using motion tracking
  Track external the path of a robot
  Track a robot manipulator
  Allow for planning
  Provide external feedback to improve the internal feedback

## Slide 24: GPS

## Slide 25: GPS
Used in mobile robots and navigation systems to determine the current position of the device relative to a global reference frame.
The system includes many satellites orbiting the Earth at about 20,000 km, a control and monitoring station on Earth, and the GPS receivers.

## Slide 26: GPS
The receiver uses the transmitted data from the satellites to calculate its position. This information can be sent directly to the control system of a mobile robot for positioning purposes and navigation.
Each satellite sends signals at precise intervals with information about the time the signal was sent and location of the satellite.
The GPS unit reads the signals sent by four satellites, and using the difference between the current time and the time at which each signal was sent calculates the distance to the satellite.
Each distance forms a sphere centred at the satellite, on which the GPS unit resides. The intersection between these spheres is the location of the GPS unit.

## Slide 27: GPS
Can be extremely accurate sub metre
  Differential GPS can improve this
    Two receivers with a fixed distance between them
    Triangulation
Only really for outside
  Just ask your phone
Should also be implemented when you can
Can take time to settle and locate satellites
Many off the shelf providers
…oh care needs to be taken with Antenna position

## Slide 28: References
Niku, S.B. , Introduction to Robotics, 2nd Edition, Wiley, New Jersey, 2011